## Slide 1: Circuit Model for a microring modulator
Simon Bélanger-de Villers
2020

## Slide 2: Notes and future works
Vary the ring radius in order to find the optimal value;
Instead of using the analytical model, use the TMM model;
Use the time domain model by B.E. Little for simple yet more accurate time domain/ large signal analysis;

## Slide 3: Circuit model of a MRM
Input parameters (scalars)
  R : Ring radius [µm];
  w : Waveguide’s ridge width [nm];
  h : Waveguide’s ridge thickness [nm];
  sh : Waveguide’s slab thickness [nm];
  g : Bus-Ring gap width [nm];
  pnC : PN Junction coverage [%];
h
sh
w
Waveguide cross section
MRM top view
g
R
Ein
Eout

## Slide 4: OOP function block diagram
MRM
MRR
MRR AP
Waveguide
PhaseShifter
Directionnal Coupler
Inherits
Instantiates in
Relations arrows
MRR : general microring resonator
MRR AP : all-pass type microring resonator
MRR AD : add-drop type microring resonator
MRM : microring modulator (all-pass)
MRR AD
Components
Circuits (or Devices)
pnC

## Slide 5: Circuits attributes and methods
MRR
Attributes
radius
roundtripLength
roundtripPhase
roundtripLoss
effectiveIndex
groupIndex
FSR
Qfactor
Methods
getRoundtripLength
getRoundtripPhase
getRoundtripLoss
MRR AD
Attributes
fdsf
Methods
fds
MRM
Attributes
fdsf
Methods
fds
: power thru-coupling coefficient
: power cross-coupling coefficient
(lossless)
: power attenuation coefficient [1/m]
: single-pass amplitude transmission

## Slide 6: Components attributes and methods
Waveguide
Attributes
ridgeWidth
ridgeThickness
slabThickness
Materials
length
bendingRadius
centralWavelength
effectiveIndex
groupIndex
intrinsicLoss
Methods
getPropagationMatrix

## Slide 7: Losses in waveguides

## Slide 8: Effective index and group index

## Slide 9: Propagation losses
Loss mechanisms in a microring modulator loaded with a PN junction
  Propagation losses [dB/cm] : Waveguide propagation losses for a doped waveguide with 0 V bias applied;
  Bending losses [dB/cm] : Losses that are dependant on the radius of curvature of the ring;
  Perturbative losses [dB/cm] : Losses that are dependant on the bias voltage applied to the PN Junction.

## Slide 10: Propagation losses specifications
Data for strip waveguides only. What would be the losses for standard rib waveguides?
Applied Nanotools NanoSOI
AMF Silicon Photonics

## Slide 11: Coupling Coefficient vs gap
220 nm
Ring Waveguide
Bus
Waveguide
500 nm
500 nm
90 nm
g
Target cross section geometry
Target top view geometry
g
10 µm
Power cross coupling coefficient vs gap for the target geometry
*We consider the coupling region to be undoped.
** Simulated using 3D FDTD (mesh 3)

## Slide 12: PN Junction
Intra-cavity modulation -> and ;
Parameters:
  Junction recipe;
  LPN : PN junction length [µm];
  cid : Intermediary dopants clearance [µm];
  chd : Heavy dopants clearance [µm];
  pnC : PN junction coverage [%].
Waveguide modulator cross section
MRM top view
R
P
N
P+
P++
N++
N+
chd
cid
chd
cid
*presume int/heavy doping clearance is symetric
Lumerical DEVICE parameters
Circuit model parameters

## Slide 13: Total Electro-Optic bandwidth
Not totally accurate: The Q factor depends on the detuning which causes a peaking effect.
The optical bandwidth will be underestimated.

## Slide 14: Phase shifter equation
: PN coverage [%] /100

## Slide 15: How to use the code
MRM
Waveguide
w
h
sh
neff
ng
R
Coupler
Phase Shifter
pnC
data
T
BW
FSR
ER
Specs
Q
RCBW
Transmission + phase
OMA
IL
PS Efficiency
Perturbative losses

## Slide 16: Supplementary - Misc
Peaking effect in microring modulators
Source : J. Müller, F. Merget, S. S. Azadeh, J. Hauck, S. R. Garcia, B. Shen, and J. Witzens. Optical peaking enhancement in high-speed ring modulators. Scientific reports, 4:6310, 2014.
: Angular frequency of the applied perturbation [rad/s]
: Angular resonant frequency of the resonator [rad/s]
: Angular frequency of the CW optical carrier from the laser [rad/s]